## Slide 1: Week 4
Bluetooth Communication
Fancy Graphics
Misc. DSP concepts
The FoneAstra
Notes: Things to improve:
Confusion about copying into/out of OS-provided buffers

## Slide 2: Final Projects
I’ve received some questions about this
  I’m very open-minded, but you should have ideas by next week
Find a buddy (or two, if you’re ambitious)
  Trios will need to do something crazier, as you have more manpower
I’ll want a written report
  These are due Tuesday, Feb 10th, but feel free to email them to me early!
  No more than one-page summaries please, we’re all busy men/women
Key points your project should hit
  Sensing/control (Both would be awesome)
  Real-time (or close) computation/processing
  Usefulness/”coolness factor” always a plus

## Slide 3: Overview
Today we’re going to learn Bluetooth
  This will allow us to control separate pieces of hardware
I’ll be handing out Arduinos called the FoneAstra
  Onboard BT, SD Card, Buzzer, Battery make it very useful for this class
We have less than 12 FoneAstras
  Therefore, you guys are really going to need to pair up and share
Students in the past have purchased their own
  So that they can keep them after class and experiment
  Talk to me if you want to know which components to buy
  Should total no more than $40 dollars overall (pre-tax)

## Slide 4: Fancy Graphics
It would be really nice if we could plot things
  Turns out, we can!
Drawing to the screen quickly is difficult however
  Getting to the point where you can draw a single line takes a LOT of code
  DirectX is just as verbose as WASAPI, and there’s even more going on
We’re not going to cover how to do this
  We’re just going to use a class I wrote

## Slide 5: LineGraph
Uses an Image to output graphics
  I’ve made up a C++ component for your use
  It uses DirectX to plot a line (400+ lines of C++!)
It’s C++/CX, so you include it via “References”
It’s quite simple to use
  Basic procedure:
    Include an Image XAML element in your XAML
    Include a LineGraph in your C# class
    Hook the LineGraph up to the Image as shown in the sample code
    Use the functions documented in the LineGraph.h file

## Slide 6: LineGraph Live Demo

## Slide 7: Asynchronous Tasks
C# has some more goodies for us
  Sometimes, we want to execute things asynchronously
    But we don’t want/need to do them simultaneously
Enter the async and await keywords
  The former modifies function declarations
  The latter modifies function calls
private async void myGreatFunction()
{
...
float[] result = await myOtherGreatFunction();
}

## Slide 8: Asynchronous Tasks
You must use async on any function with await in it
The await keyword tells the compiler “wait for this”
  Execution of the current function stops until done waiting
  Execution then resumes
Internally, this is making extensive use of Dispatcher
  The compiler reaches a condition inside of an await
  Execution stops, all code after the condition is given to the Dispatcher
  Eventually, the condition is cleared, and the Dispatcher continues
This is really useful for waiting for external events
  Files loading, shaders compiling, network resources arriving, etc…

## Slide 9: Asynchronous Tasks
async Task<int> AccessTheWebAsync()
{
HttpClient client = new HttpClient();
Task<string> data = client.GetStringAsync("http://msdn.microsoft.com");
// You can do work here that doesn't rely on [data]
DoIndependentWork();
string urlContents = await data;
// The return statement specifies an integer result.
// Any methods that are awaiting AccessTheWebAsync retrieve the length value.
return urlContents.Length;
}

## Slide 10: Asynchronous Tasks
All async methods return a Task
  This wraps around the desired return type
  Asynchronous methods return before their work is “complete”
  This allows synchronous methods to explicitly wait for the condition
  Only happens once you access the Result property
private void myGreatFunction()
{
Task<int> taskData = AccessTheWebAsync();
int data = taskData.Result;
}

## Slide 11: Asynchronous Tasks

## Slide 12: Async Live Demo

## Slide 13: Bluetooth
A Short-range wireless protocol developed by Intel
  Originally designed for The Internet Of Things, Bluetooth’s poster child was a toaster that could burn the weather on your toast in the morning
  That it would find a market in cell phones was something of a surprise
After many iterations, now achieves its goal
  Low-power, variable bandwidth, short-range, ubiquitous communication
  This makes it an attractive choice for many embedded systems
We’re going to use it to control 3rd party hardware
  The FoneAstra, a board based on the Arduino
  Contains a Bluetooth Module, pins for sensors, an SD Card mount
You are going to write the software for both sides
  The Phone to do what it does best; sensing, communication
  The Arduino to do anything and everything else

## Slide 14: Bluetooth Concepts
To communicate with the Arduino, we must:
  Enable Bluetooth on the Phone, and pair it with the Arduino
    This is a security measure to ensure Bob doesn’t use Alice’s BT headset by accident: you need to use the proper PIN to connect to it
    In practice, almost all “dumb” BT devices use 0000 or 1234 as PIN
  Open the Bluetooth interface for communication in the Arduino
    Using C, we’ll cover this later
  Search for peers, request communication with one in the Phone
    Using C#, we’ll cover this next
  Write data out to the Bluetooth device, and read data in
    On both the Phone and the Arduino

## Slide 15: Bluetooth on WP8
Once you turn the Bluetooth on, it’s just “available”
  No “initialization” step, other than ensuring that Proximity is checked
  There’s also a hidden flag we need to set in our Package manifest
Use the PeerFinder class to search nearby devices
  Used to find not only other BT devices, but also specific applications
  Operates not only on BT, but also NFC and Wifi
  We’re using only BT, so we’ll make sure to specify that
Once you’ve got a Peer, open a StreamSocket
  The most basic TCP/Bluetooth communication method
  Sends a continuous stream of data
    This is as opposed to Datagram-based communication (e.g. UDP)

## Slide 16: Streams of Data
Working with Data Streams can be tricky
  This idealized “stream” of data is chunked up into packets
    These packets are then sent to the BT radio and transmitted
    This is done transparently by the operating system
  The receiving end is notified at the packet level
    There is no way of knowing how much data to wait for
    Unless we invent a protocol to give us this knowledge!
…

## Slide 17: Streams of Data
Protocols are easy and neat
  Example protocol:
    First 4 bytes of every message is an integer with size of following data
    Next N bytes are the data, where N is the value of the original integer
    Interpreting this data is completely up to your application
  Another protocol:
    Print out data willy-nilly, know it’s done with a newline
    Read it in, appending to a buffer until you read in a newline
    Additionally, hope that your data itself does not contain a newline
data
N
data
N
data
N
data
‘\n’
data
‘\n’
data
‘\n’

## Slide 18: Bluetooth on WP8
First, we tell PeerFinder to find all paired BT devices
PeerFinder.AlternateIdentities["Bluetooth:PAIRED"] = ""
Next, get a list of all peers that satisfy those criteria:
var peers = await PeerFinder.FindAllPeersAsync();
Find the peer we want:
PeerInformation peerInfo = peers.FirstOrDefault(x =>
x.DisplayName.Contains("FoneAstra"));
Connect to that peer if not null
s = new StreamSocket();
await s.ConnectAsync(peerInfo.HostName, "1");
And now we have a socket connected!

## Slide 19: Bluetooth on WP8
To send/receive data, we use Data{Writer,Reader}
  We build these out of the StreamSocket
DataWriter output = new DataWriter(s.OutputStream);
DataReader input = new DataReader(s.InputStream);
To read data in, first Load it, then Read it:
await input.LoadAsync(4);
input.ReadBytes(byteBuffer);
int length = BitConverter.ToInt32(byteBuffer, 0);
To write data out, Write it then Store it:
byte[] data = { 100, 253, 5, 67 };
output.WriteBytes(data);
output.StoreAsync();

## Slide 20: Introduction to Arduino
Programming the Arduino is an exercise in Simplicity
  It’s straight C/C++, and really easy C++ at that!
Need two functions at minimum:
  setup() and loop()
Do Input/Output with the Serial object
Serial.print(“Hello!”)
if( Serial.available() > 0 )
char key = Serial.read()
Output beeps asynchronously with tone()
tone( BUZZER_PIN, 1000, 100 );
delay( 100 );

## Slide 21: Introduction to Arduino
Setup is simple, and boilerplate:
#include "foneastrapins.h"
void setup(void) {
//set up the HW UART to communicate with the BT module
Serial.begin(38400);
// Provide power to BT
pinMode(BT_PWR_PIN,OUTPUT);
digitalWrite(BT_PWR_PIN,HIGH);
// Turn on the red light
pinMode(RED_LED_PIN,OUTPUT);
digitalWrite(RED_LED_PIN, HIGH);
}

## Slide 22: BT/Arduino Live Demo

## Slide 23: Matched Filtering
Matched Filtering is a signal detection technique
  Uses convolution to find precise location in time of a known signal
Used extensively in communications applications
  Can be used to drastically increase signal-to-noise ratio
Very useful for attempting to find a preamble
Based on convolution, everyone’s favorite

## Slide 24: Matched Filtering
Basic idea is to have a “template” signal:
We convolve this with the input datastream
  NOTE: In this case we don’t want to flip and shift, just shift
  So if you’re using a filter object that flips for you, un-do that by flipping first
As we convolve, we look for when the result is large

## Slide 25: Matched Filtering
Shift and dot-product:
= 1

## Slide 26: Matched Filtering
Shift and dot-product:
= 1

## Slide 27: Matched Filtering
Shift and dot-product:
= 4

## Slide 28: Matched Filtering
Shift and dot-product:
= 1

## Slide 29: Matched Filtering
Shift and dot-product:
= 1

## Slide 30: Matched Filtering
This works best with certain templates
  In particular; their autocorrelation functions should be a delta
It works “okay” with other signals
  As long as your target signal is more-or-less orthogonal to interferers
  That’s quite a broad category
We’re going to use it with a terrible choice of filter
  A sinusoid
We’re going to see that it still kinda works

## Slide 31: Homework 4
Due to popular demand, is due at 6pm next Thursday
  Enjoy your extra 18 hours, but please don’t ask for help at 4pm on Thursday
This homework will involve everything we just learned
  Send messages to the Arduino over BT, making it beep in a certain pattern
  Detect the beepings of the Arduino by analyzing the audio stream
  Reconstruct the message you sent over Bluetooth
We’ll translate the message into BFSK pulses
  E.g. sinusoids at different frequencies

## Slide 32: Homework 4
There are multiple ways we could do this homework
  Just beep for ones and zeros, hope we catch them when they occur.
  Have a “preamble” that allows accurate timing synchronization
  Follow this preamble up with a data segment
The solution transmits a single bit per “packet”
  Packet has a preamble, 4.5 KHz signal for 5 ms
  Silence for 50 ms
  Packet then has a data bit
    0 -> 3.4 KHz signal for 50 ms
    1 -> 4.5 KHz signal for 50 ms
Feel free to be more adventurous

## Slide 33: Homework 4 Demo

## Slide 34: FFTW
We have a C++/CX class that can do FFT’s
  Internally uses the FFTW library, a very well-known opensource C++ library
Very straightforward to use
  Since it’s C++/CX, it will deal in C# arrays, so we can use it from C#
A few functions of merit:
  fft()
  ifft()
  fftMag()
  fftLogMag()
Combine this with LineGraph for hours of fun

## Slide 35: Using the FoneAstra
It’s built out of an Arduino Pro 3.3V w/ ATMega328
Eratta:
  Set the Arduino IDE to the correct Arduino before trying to upload code
  You might also need the FTDI drivers
  Upload code via the inner TTL header
    Bluetooth won’t be able to transmit/receive if that is still plugged in
    On the other hand, you can simulate bluetooth with that plug
  To get BT to work, disconnect your TTL cable and powercycle
  If your Arduino has a Bluetooth name like “RN-XXXX”, bring it to me
    It should say “FoneAstra–XXXX” where XXXX is the last four digits of your bluetooth address, written on the bottom of the FoneAstra

## Slide 36: Using the FoneAstra

## Slide 37: Debugging BT
This can be frustrating if something isn’t working
  Note that you can’t read in from BT on the Arduino if the USB is plugged in!
USB serial output on the Arduino is a great tool
  Open the Serial Terminal in the Arduino IDE
  Allows you to print out data from the Arduino
  Can print out to two separate Serial interfaces:
    Main Serial: What you see on the programming serial interface
      Also gets copied out to Bluetooth
    Software Serial: What you see on the second serial interface

## Slide 38: Building your own
Arduino ($25 on Amazon)
BT Module ($9 on Amazon)
Battery with female JST connector (?)
SD Card Module (?)
Feel free to substitute your own favorite parts
  These are the ones I know work, using other parts YMMV